## Slide 1: USRP FPGA project Pulse detector
Chaim bloch

## Slide 2: Pulse detector – main goal
Taking a spectrogram and summaries it to short simple data that describe the spectrum as simply as it can.
Assuming:
  Pulse keeps his amplitude the same (in a small range) for all his duration.
  Pulse can be transmitted on all frequencies in range.

## Slide 3: Pulse detector – output
  Array of pulses
    Frequency
    Toff
    Duration (long pulses – chop them to some shorter once)
    AMP
spectrogram

## Slide 4: Pulse detector– basic blocks
IQ stream
windowing
FFT
PDW creator
network
Host comp
WOLA4
Blackman
Peak detect

## Slide 5: Pulse detector– basic blocks – windowing - WOLA4
  Every sample in the entrance of the FFT is a sun of 4 windowed samples:
    Xn ,Xn+4096 ,Xn+8192 ,Xn+12288
  2 memory sectors each with 0.25 of the window (0-0.25,0.25-0.5)
  Symmetrically of the window make the NOT(index) the index for the rest of the window (wind0-0.25(not(n)= wind0.75-1(n+12288))

## Slide 6: Pulse detector– basic blocks –peak detect
  Reorder the samples and FFT shift
  Peak detect – remove skirt don’t remove ripple

## Slide 7: Pulse detector– basic blocks –spot gen
  Calculate amplitude (mean amp of the 2-9 detections (0,1 detections considered to be the rising time))
  Calculate length
  Closes gaps
  Chop CW’s
  Send approved pulses

## Slide 8: demonstration

## Slide 9: Code deep dive